## Slide 1: Automatic Recovery Trigger (ART) for Edge Servers WIP80
DMTF Redfish Forum
April 2024

## Slide 2: Disclaimer
The information in this presentation represents a snapshot of work in progress within the DMTF.
This information is subject to change without notice. The standard specifications remain the normative reference for all information.
For additional information, see the DMTF website: www.dmtf.org
© 2024 DMTF

## Slide 3: Introduction
Watchdog Timers (WDTs) are hardware/firmware/software countdown timers used to detect and recover a system when malfunctioning.
During normal operation, a system will periodically service a WDT by restarting its timer. A failed system stops servicing the WDT whose timer will eventually elapse and trigger a recovery action, such as a system reboot. WDTs are widely used in practice, especially in embedded systems.
An Automatic Recovery Trigger (ART) is a secure form of a watchdog timer aimed at Edge servers
© 2024 DMTF

## Slide 4: Concept Overview
Unlike normal WDTs, an ART timer must be serviced by a remote management controller, such as a Health Service that monitors the health of the remote Edge server. When the server misbehaves or becomes unresponsive, the Health Service will stop servicing the Edge server’s ART timer.
If the ART timer eventually elapses, ART performs three steps to automatically recover the server:
  Signals the operating system (OS) that the server will soon reboot
  Reboots the server
  Ensures the server enters a recovery environment upon booting up.
The recovery environment performs corrective actions to the platform such as system re-imaging to remove malware.
© 2024 DMTF

## Slide 5: Automatic Recovery Trigger
Automatic Recovery Trigger is a BMC timer service with certificate-based heartbeat refresh with actions to recover/re-image a malfunctioning/ compromised server
ART framework consists 3 components:
  Remote Health Service instances running in the cloud
  Optional Host-based Local service (for communication with cloud-based Health Service)
  Authenticated watchdog timer running in the BMC
Health Service issues authenticated tickets (signed) to BMC
If not serviced, BMC watchdog times out and re-images/recovers host OS
Uncompromised OS
compromised OS
© 2024 DMTF

## Slide 6: Proposed Redfish Changes
Added new schema AutomaticRecoveryTrigger under Systems (URI: /redfish/v1/Systems/{ComputerSystemId}/AutomaticRecoveryTrigger)
User can utilize GET to Read the Nonce
User can utilize POST to send ticket
Remote Health Service can utilize encryption to send ticket, and he encryption/decryption of the ticket is defined by orchestration.
© 2024 DMTF

## Slide 7: Automatic Recovery Trigger – ReadART
Example mockup
Example Curl Command:
© 2024 DMTF

## Slide 8: Automatic Recovery Trigger - Ticket
Example Ticket
Example Curl Command:
curl -H"X-Auth-Token: $token" -H "Content-Type: application/json" --request POST --data {\”Ticket”:{ \"ARTId\":\“16a770fa-3574-4f53-a81a-d163a03573ad\", \"TriggerTimeoutSeconds\":86400, \"TriggerTimeoutAction\": {\"ActionType\": \"BootFromVirtualMedia\", \"ActionData\": \"https://media.contoso.com/RecoveryImage-20240211.iso\"}} , \"GraceTimeoutPastSeconds\": 3600, \"GraceTimeoutAction\": { \"ActionType\": \“RedfishEvent\", \"ActionData\": \""}, \"Nonce\":\“d75085f449cd9a6e2f6d92e8c93e39fc\", \“Signature\":\“mF_9.B5f-4.1JqM\"} https://${bmc}/redfish/v1/Systems/{ComputerSystemId}/AutomaticRecoveryTrigger/Actions/AutomaticRecoveryTrigger.SendTicket
© 2024 DMTF

## Slide 9: Automatic Recovery Trigger – Timeout Actions
Timeout Actions for both Trigger and Grace Period :
  BootFromVirtualMedia : Make host boots from virtual media
  NotifyAgentURL : all the URL to notify Agent as an alternative to Booting from Virtual Media
© 2024 DMTF

## Slide 10: Q&A & Discussion